## Slide 1: AWAKE: Advanced Proton Driven Plasma Wakefield Acceleration Experiment at CERN
Edda Gschwendtner
on behalf of the AWAKE Collaboration

## Slide 2: Outline
Introduction
AWAKE at CERN
AWAKE: 1st Phase
AWAKE: 2nd Phase
The Experimental Facility at CERN
Planning and Next Steps
Summary

## Slide 3: Main Driver for PWFA: Linear Collider
Linear collider based on plasma wakefield acceleration:
Plasma can sustain up to three orders of magnitude higher gradient
   Much shorter linear colliders!
ILC
 Build a High energy collider at TeV range!
Linear collider based on RF cavities:
Accelerating field limited to <100 MV/m
  Several tens of kilometers for future linear colliders
  For example ILC:
    31km long
    500 GeV electrons
    16 superconducting accelerating cavities made of pure niobium
    Gradient of 35 MV/m
1000mm

## Slide 4: Main Driver for PWFA Research: Linear Collider
* J.P.Delahaye, E. Adli et al., White Paper input to US Snowmass Process 2013
3
500
3000
GeV
km
8
Aim to reach accelerators in the TeV range!

## Slide 5: Plasma Wakefield Acceleration Principle
Plasma wave is excited by a relativistic particle bunch.
Space charge of drive beam displaces plasma electrons.
Plasma electrons attracted by plasma ions, and rush back on-axis.
Ez
 deceleration
 acceleration
Size of the accelerating structure is set by the plasma density:
plasma wavelength lp =1mm, (for typical plasma density of np = 1015cm-3 )
Produce ‘mini cavities’ inside the plasma cell
To excite large amplitude wakefields, proton bunch length sz ~ lp = 1mm

## Slide 6: Some Experimental Results
Experimental results show success of PWFA and its research
  SLAC beam: 42 GeV, 3nC @ 10 Hz, sx = 10µm, 50 fs
High-Efficiency acceleration of an electron beam in a plasmas wakefield accelerator
M. Litos et al., doi, Nature, 6 Nov 2014, 10.1038/nature 13992
  Total efficiency is <29.1%> with a maximum of 50%.
  Final energy spread of 0.7 % (2% average)
Notes: Test key performance parameters for the witness bunch acceleration:
  Gradient
  Efficiency
  Energy spread
  Emittance
Laser ionized Lithium vapour plasma cell:
  36 cm long, Density: 5 1016 cm-3, lp = 200 µm
Drive and witness beam:
  20.35 GeV, D and W separated by 160 µm
  1.02nC (D), 0.78nC (W)

## Slide 7: Electron Beam Driven PWA
There is a limit to the energy gain of a witness bunch in the plasma:
  Today’s electron beams usually < 100 J level.
To reach TeV scale with electron driven PWA: also need several stages, but need to have
  relative timing in 10’s of fs range
  many stages
  effective gradient reduced because of long sections between accelerating elements….
Witness beam
Drive beam: electron/laser
Plasma cell
Plasma cell
Plasma cell
Plasma cell
Plasma cell
Plasma cell

## Slide 8: Proton Beam Driven PWA
Proton beams carry much higher energy:
19kJ for 3E11 protons at 400 GeV/c.
  Drives wakefields over much longer plasma length, only 1 plasma stage needed.
Simulations show that it is possible to gain 600 GeV in a single passage through a 450 m long plasma using a 1 TeV p+ bunch driver of 10e11 protons and an rms bunch length of 100 mm.
Witness beam
Drive beam: protons
Plasma cell
A. Caldwell, K. Lotov, Physics of Plasma, 18,103101 (2011)

## Slide 9: Beam-Driven Wakefield Acceleration: Landscape
Facility | Where | Drive (D) beam | Witness (W) beam | Start | End | Goal
AWAKE | CERN, Geneva, Switzerland | 400 GeV protons | Externally injected electron beam (PHIN 15 MeV) | 2016 | 2020+ | Use for future high energy e-/e+ collider. Study Self-Modulation Instability (SMI). Accelerate externally injected electrons. Demonstrate scalability of acceleration scheme.
SLAC-FACET | SLAC, Stanford, USA | 20 GeV electrons and positrons | Two-bunch formed with mask (e-/e+ and e--e+ bunches) | 2012 | Sept 2016 | Acceleration of witness bunch with high quality and efficiency Acceleration of positrons FACET II proposal for 2018 operation
DESY-Zeuthen | PITZ, DESY, Zeuthen, Germany | 20 MeV electron beam | No witness (W) beam, only D beam from RF-gun. | 2015 | ~2017 | Study Self-Modulation Instability (SMI)
DESY-FLASH Forward | DESY, Hamburg, Germany | X-ray FEL type electron beam 1 GeV | D + W in FEL bunch. Or independent W-bunch (LWFA). | 2016 | 2020+ | Application (mostly) for x-ray FEL Energy-doubling of Flash-beam energy Upgrade-stage: use 2 GeV FEL D beam
Brookhaven ATF | BNL, Brookhaven, USA | 60 MeV electrons | Several bunches, D+W formed with mask. | On going |  | Study quasi-nonlinear PWFA regime. Study PWFA driven by multiple bunches Visualisation with optical techniques

## Slide 10: Outline
Introduction
AWAKE at CERN
AWAKE: 1st Phase
AWAKE: 2nd Phase
The Experimental Facility at CERN
Planning and Next Steps
Summary

## Slide 11: AWAKE
AWAKE: Advanced Proton Driven Plasma Wakefield Acceleration Experiment
Proof-of-Principle Accelerator R&D experiment at CERN
  First proton driven wakefield experiment worldwide
  Demonstration of high-gradient acceleration of electrons
AWAKE Collaboration: 16 Institutes world-wide
11
Novosibirsk
Vancouver
Oslo
Hamburg, Greifswald
Dusseldorf
Munich
CERN
Lisbon
Manchester
London
Glasgow

## Slide 12: AWAKE at CERN
CNGS
2006
produce
muon-neutrinos
measure
tau-neutrinos
CERN
Gran Sasso
732km
AWAKE in CNGS Facility (CERN Neutrinos to Gran Sasso)
CNGS physics program finished in 2012
  CNGS approved for 5 years: 2008 – 2012
  Expect ~8 tau-neutrinos, 4 published so far

## Slide 13: AWAKE at CERN
Running underground facility
Desired beam parameters
 adequate site for AWAKE
AWAKE
Approved in August 2013
First beam expected in 2016
Initial program for 3-4 years

## Slide 14: AWAKE at CERN
Running underground facility
Desired beam parameters
 adequate site for AWAKE
AWAKE experiment
dump
~1100m
SPS
LHC
protons

## Slide 15: Outline
Introduction
AWAKE at CERN
AWAKE: 1st Phase
AWAKE: 2nd Phase
The Experimental Facility at CERN
Planning and Next Steps
Summary

## Slide 16: SPS Proton Beam: Drive Beam
Nominal SPS Proton Beam Parameters | 
Momentum | 400 GeV/c
Protons/bunch | 3 1011
Bunch length | sz = 0.4 ns (12 cm)
Bunch size at plasma entrance | s*x,y = 200 mm
Normalized emittance (r.m.s.) | 3.5 mm mrad
Relative energy spread | Dp/p = 0.35%
Long proton beam sz = 12cm! Compare with plasma wavelength of l = 1mm.
 Experiment based on Self-Modulation Instability!
  Modulate long bunch to produce a series of ‘micro-bunches’ in a plasma with a spacing of plasma wavelength lp.
    Strong self-modulation effect of proton beam due to transverse wakefield in plasma
    Starts from any perturbation and grows exponentially until fully modulated and saturated.
 Immediate use of the SPS beam!

## Slide 17: Plasma Source: Rubidium Vapor Source
Required:
Dn/n = DT/T ≤ 0.002
Density adjustable from 1014 – 1015 cm-3
10 m long, 4 cm diameter
Plasma formed by field ionization of Rb
  Ionization potential FRb = 4.177eV
  above intensity threshold (Iioniz = 1.7 x 1012W/cm2) 100% is ionized.
Plasma density = vapor density
System is oil-heated: 150˚ to 200˚ C
  keep temperature uniformity
  Keep density uniformity

## Slide 18: Plasma Source: Rubidium Vapor Source
Fast valves at both ends
 separation of plasma from SPS beam vacuum.
 Must be opened when laser/electron/proton passes through.
3m prototype at MPI Munich
Ultra-fast (15 ms) valves
> 40 000 cycles!

## Slide 19: Laser Beam
Laser intensity must exceed ionization intensity at the plasma end (L=10m) over a plasma radius of r > 3s = 600 µm.
Laser Beam | 
Laser type | Fiber Ti:Sapphire
Pulse wavelength | l0 = 780 nm
Pulse length | 100-120 fs
Pulse energy (after compr.) | 450 mJ
Laser power | 4.5 TW
Focused laser size | sx,y = 1 mm
Rayleigh length ZR | 5 m
Energy stability | ±1.5% r.m.s.
Repetition rate | 10 Hz
Laser system in MPI, Munich

## Slide 20: Combining Drive Beam, Plasma Source, Laser: Proton Bunch Self-Modulation
Self-Modulation Instability (SMI):
Laser beam co-moving within the proton bunch effectively seeds the SMI
  Laser pulse creates the ionization front
  Ionization front acts as if long proton bunch is sharply cut
  Laser pulse excites wakes to directly seed the self-modulation instability
  grows exponentially until fully modulated and saturated.
N. Kumar, A. Pukhov, K. Lotov, Phys. Rev. Letters (2010):
lp = 1.2 mm
Self-modulated proton bunch resonantly driving plasma wakefields.
laser pulse
proton bunch
gas
plasma

## Slide 21: AWAKE: 1st Experimental Phase
Laser
dump
SPS
protons
10m plasma cell
Proton
beam
dump
Laser
Proton diagnostics
OTR, CTR, TCTR
p
Perform benchmark experiments using proton bunches to drive wakefields for the first time ever.
Understand the physics of self-modulation instability processes in plasma.
Plasma electron density rplasma
Proton beam density rbeam
Self-modulated proton bunch resonantly driving plasma wakefields.
laser pulse
proton bunch
gas
plasma
J. Vieira et al PoP 19063105 (2012)

## Slide 22: AWAKE Experimental Layout: 1st Phase
Laser
dump
SPS
protons
10m plasma cell
Proton
beam
dump
Laser
Proton diagnostics
OTR, CTR, TCTR
p
Maximum amplitude of the accelerating field Ez as a function of position along the plasma.
Saturation of the SMI at ~4m.
Laser and proton beam synchronized at the 100 ps level.
Laser and proton beam co-axial over the full length of the plasma cell:
  100 mm and 15 mrad pointing accuracy
  High resolution diagnostics to perform and monitor relative alignment
Plasma density uniformity better than 0.2%
laser pulse
proton bunch
gas
plasma

## Slide 23: AWAKE Experimental Layout: 1st Phase
Laser
dump
SPS
protons
10m plasma cell
Proton
beam
dump
Laser
Proton diagnostics
OTR, CTR, TCTR
p
Maximum amplitude of the accelerating field Ez as a function of position along the plasma.
Saturation of the SMI at ~4m.
Laser and proton beam synchronized at the 100 ps level.
Laser and proton beam co-axial over the full length of the plasma cell:
  100 mm and 15 mrad pointing accuracy
  High resolution diagnostics to perform and monitor relative alignment
Plasma density uniformity better than 0.2%
 Measure self-modulated proton beam
laser pulse
proton bunch
gas
plasma

## Slide 24: Self-Modulation Instability Diagnostics
Direct Measurement of self-modulation instability of the proton beam
   results in radial modulation of the proton beam (micro-bunches)
  Measured by using the radiation emitted by the bunch when traversing a dielectric interface or by directly sampling the bunch space charge field.  streak-camera.
sp ~ 400 ps
4 ps
CTR & TCTR
OTR
Optical Transition Radiation (OTR)
Coherent Transition Radiation (CTR)
Transverse Coherent Transition Radiation (TCTR)
Laser
dump
SPS
protons
10m
SMI
Proton
beam
dump
Laser
p
BTV
BTV
Laser
dump
Indirect Measurement by observing the proton bunch defocusing downstream the plasma
   Proton bunch: 1mrad divergence

## Slide 25: Outline
Introduction
AWAKE at CERN
AWAKE: 1st Phase
AWAKE: 2nd Phase
The Experimental Facility at CERN
Planning and Next Steps
Summary

## Slide 26: AWAKE Experimental Layout: 2nd Phase
Probe the accelerating wakefields with externally injected electrons, including energy spectrum measurements for different injection and plasma parameters.
Laser
dump
e- spectrometer
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
Proton diagnostics
OTR, CTR, TCTR
p
laser pulse
proton bunch
gas
plasma
electron bunch

## Slide 27: Witness Beam: Electron Source
PHIN Photo-injector for CTF3/CLIC:
  Charge/bunch: 2.3 nC
  Bunch length: 10 ps
  1800 bunches/train, 1.2µs train-length
  Program will stop end 2015
Fits to requirements of AWAKE
Photo-injector laser derived from low power level of plasma ionization laser system.
Length ~ 4 m
FC
E, DE
MS
BPR
Laser +Diagnostics
RF GUN
Emittance
Incident, Reflected Power and phase
Spectrometer
Corrector
MTV
VPI
FCT
Accelerator
MTV,
Emittance
Matching triplet
BPR
BPR
Incident, Reflected, transmitted Power
Klystron from CTF3
electron beam line
1m booster linac
(Cockcroft)
e-beam diagnostics
Laser beam for electron source | 
Laser type | Ti:Sapphire Centaurus
Pulse wavelength | l0 = 260 nm
Pulse length | 10 ps
Pulse energy (after compr.) | 500 mJ
Electron source cathode | Copper
Quantum efficiency | 3.00 E-5
Energy stability | ±2.5% r.m.s.

## Slide 28: AWAKE Experimental Layout: 2nd Phase
Probe the accelerating wakefields with externally injected electrons, including energy spectrum measurements for different injection and plasma parameters.
Laser
dump
e- spectrometer
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
Proton diagnostics
OTR, CTR, TCTR
p
Electron beam | 
Momentum | 16 MeV/c
Electrons/bunch (bunch charge) | 1.2 E9 (0.2 nC)
Bunch length | sz =4ps (1.2mm)
Bunch size at focus | s*x,y = 250 mm
Normalized emittance (r.m.s.) | 2 mm mrad
Relative energy spread | Dp/p = 0.5%
Beta function | b*x = b*y = 0.4 m
Dispersion | D*x = D*y = 0
laser pulse
proton bunch
gas
plasma
electron bunch

## Slide 29: AWAKE Experimental Layout: 2nd Phase
Laser
dump
e- spectrometer
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
Proton diagnostics
OTR, CTR, TCTR
p
Laser and electron beam synchronized at the < 1 ps level.
Electron bunch is externally injected into the plasma cell, on-axis and collinearly with the proton and laser beam.
On-axis injection point is upstream the plasma cell.
laser pulse
proton bunch
gas
plasma
electron bunch

## Slide 30
On-axis injection: animation of trapping and acceleration
  Electrons are trapped from the very beginning by the wakefield of seed perturbation
  Trapped electrons make several synchrotron oscillations in their potential wells
  After z=4 m the wakefield moves forward in the light velocity frame
black points – injected electrons, false colors – wakefield potential
x, cm
-16.4
-17
r, mm
0
2
AWAKE Experimental Layout: 2nd Phase
K. Lotov, LCODE

## Slide 31: AWAKE Experimental Layout: 2nd Phase
Laser
dump
e- spectrometer
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
Proton diagnostics
OTR, CTR, TCTR
p
Laser and electron beam synchronized at the < 1 ps level.
Electron bunch is externally injected into the plasma cell, on-axis and collinearly with the proton and laser beam.
On-axis injection point is upstream the plasma cell.
Energy of the electrons gained along the 10 m long plasma cell.
laser pulse
proton bunch
gas
plasma
electron bunch

## Slide 32: AWAKE Experimental Layout: 2nd Phase
Laser
dump
e- spectrometer
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
Proton diagnostics
OTR, CTR, TCTR
p
Laser and electron beam synchronized at the < 1 ps level.
Electron bunch is externally injected into the plasma cell, on-axis and collinearly with the proton and laser beam.
On-axis injection point is upstream the plasma cell.
Trapping efficiency: 10 – 15 %
Average energy gain: 1.3 GeV
Energy spread: ± 0.4 GeV
Angular spread up to ± 4 mrad
Large acceptance spectrometer (aperture and magnetic field)
laser pulse
proton bunch
gas
plasma
electron bunch

## Slide 33: AWAKE Experimental Layout: 2nd Phase
Laser
dump
e- spectrometer
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
Proton diagnostics
OTR, CTR, TCTR
p
Laser and electron beam synchronized at the < 1 ps level.
Electron bunch is externally injected into the plasma cell, on-axis and collinearly with the proton and laser beam.
On-axis injection point is upstream the plasma cell.
Trapping efficiency: 10 – 15 %
Average energy gain: 1.3 GeV
Energy spread: ± 0.4 GeV
Angular spread up to ± 4 mrad
Large acceptance spectrometer (aperture and magnetic field)
 Measure accelerated electrons
laser pulse
proton bunch
gas
plasma
electron bunch

## Slide 34: Witness Beam Acceleration Diagnostics
Probe the accelerating wakefields with externally injected electrons
 Electron spectrometer
Measure peak energy and energy spread of electrons.
Spectrometer magnet separates electrons from proton beam-line.
Magnet: 15 ton, 1.84 T, 3.80 Tm, L=1670 mm, W=1740 mm
p
e-
Scintillator screen
Camera
Dispersed electron impact on scintillator screen.
Resulting light collected with intensified CCD camera.

## Slide 35: Outline
Introduction
AWAKE at CERN
AWAKE: 1st Phase
AWAKE: 2nd Phase
The Experimental Facility at CERN
Planning and Next Steps
Summary

## Slide 36: AWAKE Experimental Facility at CERN
AWAKE experiment
protons
protons
Laser
dump
e- spectrometer
e-
SPS
protons
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
Proton diagnostics
OTR, CTR, TCTR
p
towards proton beam dump

## Slide 37: Proton Beam Line
750m proton beam line
Change of the proton beam line only in the downstream part (~80m)
 Displace existing magnets of the final focusing to fulfill optics requirements at plasma cell
Laser-proton merging 20m upstream the plasma cell
CNGS Layout
AWAKE Layout
 Move existing dipole and 4 additional dipoles to create a chicane for the laser mirror integration.

## Slide 38: Laser System
p+ beam
e- beam
laser
laser
New tunnel
Ti: Sapphire laser system:
Laser with 2 beams (for plasma and e-gun)
Delay line in either one of both beams
Focusing telescope (lenses, in air) before compressor
35 meter focusing
Optical compressor (in vacuum)
Optical in-air compressor and 3rd harmonics generator for electron gun
Complete UHV vacuum system up to 10-7 mbar starting from optical compressor

## Slide 39: Electron Beam Line
Completely new beam line and tunnel:
  Horizontal angle of 60 deg,
  20% slope of the electron tunnel  1m level difference
  7.2% slope of the plasma cell
  ~5 m common beam line between electron and proton
Common diagnostics for proton (high intensity, 3E11 p) and electron beam (low intensity, 1.2E9 e)
Flexible electron beam optics: focal point can be varied by up to 6 m inside the plasma cell
Electron beam envelope (H, V)
Plasma cell

## Slide 40: Electron Beam Line
Excavation June – October 2014

## Slide 41: Electron Beam Line

## Slide 42: Outline
Introduction
AWAKE at CERN
AWAKE: 1st Phase
AWAKE: 2nd Phase
The Experimental Facility at CERN
Planning and Next Steps
Summary

## Slide 43: AWAKE Timeline
AWAKE was approved in August 2013
1st Phase: First proton and laser beam in 2016
2nd Phase: first electron beam in 2017
Physics program for 3 – 4 years
Run-scenario | Nominal
Number of run-periods/year | 4
Length of run-period | 2 weeks
Total number of beam shots/year (100% efficiency) | 162000
Total number of protons/year | 4.86×1016 p
Initial experimental program | 3 – 4 years

## Slide 44: Next Steps
Split-cell mode: SMI in 1st plasma cell, acceleration in 2nd one.
New scalable uniform plasma cells (helicon or discharge plasma cell)
Step in the plasma density  maintains the peak gradient
Need ultra-short electron bunches (> 300fs)  bunch compression  Almost 100% capture efficiency
Plasma density profile
Maximum wakefield amplitude

## Slide 45: Outline
Introduction
AWAKE at CERN
AWAKE: 1st Phase
AWAKE: 2nd Phase
The Experimental Facility at CERN
Planning and Next Steps
Summary

## Slide 46: Summary
AWAKE is proof-of-principle accelerator R&D experiment currently being built at CERN
  First proton-driven wakefield acceleration experiment worldwide.
  The experiment opens a pathway towards plasma-based TeV lepton collider.
   Final Goal: Design high quality & high energy electron accelerator based on acquired knowledge.
AWAKE using CERN infrastructure
  400 GeV SPS proton beam as drive beam
  10-20 MeV electrons as witness beam
  4.5 TW laser beam for plasma ionization and seeding of the SMI
AWAKE program
  Study the physics of self-modulation instability as a function of plasma and proton beam parameters (1st Phase, 2016)
  Probe the longitudinal accelerating wakefields with externally injected electrons (2nd Phase, 2017-2018)
  Develop long scalable and uniform plasma cells, production of shorter electron and proton bunches (2020)

## Slide 47
Spare Slides

## Slide 48: Proton/Electron/Laser Synchronization
Synchronization between proton beam and laser pulse: ~ 100 ps (cf. proton bunch length 1s~400ps).
  SPS beam must synchronize to the AWAKE reference just before extraction.
Synchronization between electron beam and laser pulse: ~ 100 fs (cf. plasma period ~4ps)
  For deterministic injection of e- bunch into plasma wakefields
  Achieved by driving the RF-gun of the electron source with a laser pulse derived from same laser system as used for plasma ionization.
Exchange of synchronization signals on ~3 km long fibres between the AWAKE facility and SPS RF Faraday Cage in the control room
laser pulse (100fs)
proton bunch (1s ~400ps)
gas
Plasma
Electron bunch (1s~4ps)