## Slide 1: ILC detectors
Imad Laktineh
Institut de Physique Nucléaire de Lyon, France

## Slide 2
Tesla, GLD
First document
1998
2001
Tesla TDR
2003
SiD proposed
2006
Report of 4 concepts
LDC, GLD, SiD,4th
2007
LDC(Tesla) & GLD
 ILD
2009
LOI delivered
ILD & SiD validated
2013
DBD
delivered
History of ILC concepts
20??
Decision

## Slide 3
Philosophy of the ILC detectors
Detectors should be precision and discovery
tools beyond the LHC scope.
Relevant Physics phenomena in the TeV
energy range are associated to multi jet
final states  Jet energy measurement
is the most important item.
Particle Flow Algorithm is adopted in both
SiD and ILD concepts. PFA: Construction of individual
particles and estimation of their energy/momentum
in the most appropriate sub-detector.
PFA requires the different sub-detectors including calorimeters to be highly granular.
PFA uses their granularity to separate neutral from charged contributions and exploits
the tracking system to measure with precision the energy/momentum of charged particles.

## Slide 4
Philosophy of the ILC detectors
Detectors should be precision and discovery
tools beyond the LHC scope.
Relevant Physics phenomena in the TeV
energy range are associated to multi jet
final states  Jet energy measurement
is the most important item.
Particle Flow Algorithm is adopted in both
SiD and ILD concepts. PFA: Construction of individual
particles and estimation of their energy/momentum
in the most appropriate sub-detector.
PFA requires the different sub-detectors including calorimeters to be highly granular.
PFA uses their granularity to separate neutral from charged contributions and exploits
the tracking system to measure with precision the energy/momentum of charged particles.

## Slide 5
Charged tracks resolution ∆p/p ~ few10-5
Photon(s) energy resolution ∆E/E ~ 12% / E
Neutral hadrons energy resolution ∆E/E ~ 45% / E
Ejet = Echarged t + E + Eh0
fraction 65% 26% 9%
Why tracking is so important?

## Slide 6
Philosophy of the ILC detectors : Requirements
Vertex detector : excellent resolution
sIP(rf) = 5+10/(p sin2/3(q)) mm
b-tag, c-tag,… for H  bb, cc, tt studies
Tracker : excellent precision measurement of pt
s(1/pt) =10-5 GeV-1
H mass recoil, e+ e-  H Z m+ m- + anything
Calorimeters : highly granular but still providing
good measurement of neutrals
sE/E = 30%/E
The whole detector should be hermitic, compact
with moderate power consumption
30%/E

## Slide 7
Power-Pulsing
Important feature of ILC detectors to reduce power consumption and heating for highly-granular detectors
Electronics switched on just before the bunches train and off after
A factor 100-200 power reduction could be achieved.

## Slide 8
ILD SiD

## Slide 9
)

## Slide 10
ILD SiD
Precision vertex detectors
CMOS MAPs, FPCCD, DEPFET 3D, chronopixel,DEPFET, MAPs
Tracker
TPC (GEM,MMEGAS,MAPs) Silicon
many measurement points Few points but very precise
Calorimeters
ECAL: Si-W, Sc-W ECAL: Si-W
AHCAL: Sc-Steel, SDHCAL-GRPC,.. DHCAL-GRPC
Size&Magnet
Large size, 3.5 Tesla Compact, 5 tesla

## Slide 11
Tracker Silicon detectors : SiD
Vertex detector
Pixel Silicon
5 Barrel layers, 4 Disk, 3 forward Disks
Resolution better than 5 mm
Total power consumption 20 W
Air-cooled, DC-DC or serial powering.
Tracker : All-Silicon
Micro-strip detectors
5 Barrel layer, 4 Disks
Gas-cooled
Ladder structure

## Slide 12
Tracker Silicon detectors : SiD
Less than 20% X0 in the active area.
q
s(1/pt) is better than 1.5 10-5 GeV-1
99% efficiency over most of the phase space
Impact parameter resolution of 2 mm
Robustness against background

## Slide 13
Technologies proposed for the SiD vertex detector
Vertical Integrated Pixel (VIP) :
Two layer 3D ASIC bonded to silicon wafer (500 mm thick)
ASIC is 34 mm thick
24x24 mm2 pixel
192x192 array
Single pixel time stamping
Successfully read out all 192x192 = 36,864 pixels
Token passes through at 189ps/pixel
Sees source
Issues with test pulse masking,

## Slide 14
Chronopixel
Monolithic CMOS pixel sensor with integrated
electronics able to measure charge left by the particle
in the pixel and record the time of each hit
Based on using deep Pwell to prevent competing charge collection by PMOS transistors
Calibration process is ok
Readout is achievable during interval of bunch trains.
Timestamp recording speed is higher (7.23 MHz) than needed
Power-pulsing tested with no bad consequence on comparator performances.
Moderate power consumption could be obtained
with the NMOS electronics (without deep P-well techno.)
Issue with going to 90 nm technology (sensor capacitor)
which limits the signal/noise ratio but solution is there.
Prototype 3 intends to study 6 architectures
(deep, shallow NWELL, NTN,…
Technologies proposed for the SiD vertex detector

## Slide 15
Tracker Silicon detectors : ILD
Central Si Tracker System (vertex detector)
3 ladders of double layers (6 pixel layers)
|cos(q)| <.97 for inner layer, |cos(q)| <.9 for outer layer
Inner radius ~1.6 cm, outer radius ~ 6 cm
3mm resolution in the inner layer
Material budget ~ 0.3%X0/ladder layer : light support and genuine cooling system.
A pixel occupancy not exceeding a few %

## Slide 16
Central Si Tracker System (vertex detector)
3 ladders of double layers (6 pixel layers)
|cos(q)| <.97 for inner layer, |cos(q)| <.9 for outer layer
Inner radius ~1.6 cm, outer radius ~ 6 cm
3mm resolution in the inner layer
Material budget ~ 0.3%X0/ladder layer : light support and genuine cooling system.
A pixel occupancy not exceeding a few %
Time stamping
Proposed technologies: CPS, FPCCD, DEPFET,MAPs
Tracker Silicon detectors : ILD

## Slide 17
Forward Tracking Detector (vertex detector) FTD
2 pixel disks (0.25-0.5%X0/Disk)
5 false double-sided layers of Si strips (0.65%X0/Disk)
100 W/disk when power-pulsed
Same technologies proposed as for the pixel
detectors
Endcap Tracking System (ETS), Inner Tracker (SIT),
Si External Tracker (SET)
Additional precise measurements, forward tracking
improvement, time stamping
Pad size of 10x10 cm2, 50mm pitch and 200 mm thickness.
Material budget ~ 0. 65%X0/layer.
Resolution ~7mm
Tracker Silicon detectors : ILD

## Slide 18
Technologies proposed for the ILD vertex detector
DEPFET: all-silicon vertex ladder:
Ultra-thin self-supporting Silicon sensor created from Si-Oxide-Si
sandwich made of a sensor and a handle wafer after grinding
and applying lithography process.
Signal and power lines are integrated on Silicon and ASICs directly bonded on top
Pixel size : 20x20mm2
Resolution (rf) : 2.3 3.5 mm
Readout speed (25-100 ms)
Material budget : 0.15%X0/s.layer
First large (512x192 pixels), thin (50 DEPFET mm) multi-chip ladder successfully tested at DESY in 2014
DEPFET technology is chosen for BELLEII.
DCD (Drain Current Digitizer),
256 ch, 8-bit ADC/ch,
UMC 180 nm, rad hard
DHP (Digital Data Processor)
TSMC 65nm, zero suppression,
timing and trigger control
SwitcherB, Row control,
32X2 ch, Gate&Clear
AMS/IBM 180 nm
Occupancy :0.13 hit/mm2/s
Rolling shutter mode, R.O 50 ns/row
Rad. Hard
P.Pulsing, active cooling (EOS)

## Slide 19
Technologies proposed for the ILD vertex detector
CMOS Pixel Sensor (CPS):
Developed in 0.35 nm, the Mimosa26 chip
fulfills ILC requirements
New chip in 180 nm is being developed
( 2-4 faster and 60% power cons. less)
Pixel size ~ 16x16-16-64 mm2
Readout speed (112 ms)
Material budget : 0.6%X0/d.layer
(0.35%X0 with a new version)
Occupancy :0.13 hit/mm2/s
Rolling shutter mode
Rad. Hard tested
3-4 mm position resolution, 0.05-0.2° angular resolution obtained in 2012
TB at SPS. New versions of Mimosa have been successfully tested
Future activities (using output of R&D for ALICE-ITS): Finalized pixel size for different layers, material budget, integration time, power-pulsing and integration issues
Plume coll.
Eudet tel., STAR vertex detector

## Slide 20
Technologies proposed for the ILD vertex detector
FPCCD:
CCD technology with tiny pixel to provide
excellent two-track separation and low
occupancy of beam-related background
Targeted pixel size (5x5 mm2 for the inner layers,10x10 mm2 for the external layers)
12 and 9.6 mm pixel size were successfully
tested
Fully depleted 15 mm thick epitaxial sensor
Low occupancy. No need to fast electronics. Readout between bunch trains (200 ms).
16ch-ASIC to read 16x128x2500 pixels
Active circuit localized on one edge
S/N>10
10 nW/pixel
Operated at -40°C
Two-phase CO2 cooling (2 mm tube)
Low-pass filter
Double-correlated
Samplers

## Slide 21
Technologies proposed for the ILD & SiD Disks
ILD :
DEPFET petal
R&D on reducing the
material budget&cooling
2D position sensitive microstrip sensor
SiD :
Silicon strip model with hyprid-less design
Bump bonded FE to the sensor
Bias Connection
kPix Connection

## Slide 22
ILD TPC tracker
Time Projection Chamber (TPC) is chosen as the
central tracker of ILD
3D tracks (rfz) can be built thanks to many
hits (∼200/Track)
s(rf) of 100 mm (60 mm at z=0) is expected
s(z) of 1400 mm (400 mm at z=0) is expected
s(1/pt) ∼10-4 GeV-1
dE/dx information is provided (particle identification)
Readout pad size ∼ 1x6 mm2  106 pads/side
Material budget : 5%X0 in central region and less
than 25%X0 in the endplate region
Cooling is needed: two-phase CO2 is a possibility.
Two main options for gas amplification are considered :
GEM, Micromegas
0.4m <R< 1.8m
|z|< 2.15 m

## Slide 23
GEM proposals
Wet-etched Triple-GEM
Laser-etched Thick Double-GEM
GEM+Timepix
R&D to reduce the field deformation on the module edges
Wire ring is proposed.
R&D to reduce the field deformation due
to the presence of positive ions by using
a gate
Micromegas proposals
Resistive Anode Micromegas
Ingrid (MM on Timepix)
With a wire ring

## Slide 24
Very active Test Beam measurements
using PCMAG@desy
= 72 cm, L = 58 cm, B=1T
A TPC prototype with:
Modular End Plate : Up to 7 modules
(similar in size to the ILC final ones)
HV, gas and slow control system
Cosmic&beam trigger
Laser calibration system
Cooling system TRACI 2PCO2
2 TimePix octoboards:
1 mounted on MM& 1 on GEM
3 modified GEM modules tested
7 MM modules tested
Similar results obtained with the different technologies
Ongoing R&D :
New electronics with Power-Pulsing to be tested
Mechanics and low budget material

## Slide 25
Technologies proposed for ILD&SiD calorimeters
ECAL for SiD
X-talk to be reduced by better shielding
New scheme to have rectangular sensor (modified cells on the edge)
Mechanical structure study needed
1024 KPiX ASIC
Power-pulsed
TB scheme : 9 layers SiW
3-electron event

## Slide 26
Technologies proposed for ILD&SiD calorimeters
HCAL for SiD
40 layers of 2 cm stainless steel interleaved with
planes made of Glass RPC and their embedded readout 1-bit electronics allowing a lateral segmentation of 1 cm2
An advanced physical (embedded electronics) prototype of 54 was built and successfully run.
Other options with GEM and micromegas detectors are also proposed as active layers for the SiD HCAL
Several layers of mm were built and tested using 2-bit readout electronics. Few GEM planes are also in preparation.
Scintillator tiles is also an option.
Dual readout is also an option for both ECAL&HCAL
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation

## Slide 27
Technologies proposed for ILD&SiD calorimeters
ECAL for ILD
30 layers of tungsten (24X0) interleaved with
-Pixellated Silicon of 5x5 mm2,
A physics prototype (1x1 mm2 cell size) with a deported electronics was built and successfully tested.
A technological prototype fulfilling the ILD DBD requirement is being developed :
Self-supporting structure (alveolar)
Embedded power-pulsed electronics
Large surface detector
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
Energy resolution =
16.5/sqrt(E)+1.1%
Linearity <1%
Several TB took place at DESY

## Slide 28
Technologies proposed for ILD&SiD calorimeters
ECAL for ILD
30 layers of tungsten (24X0) interleaved with
of 5x45 mm2 scintillator strip with alternating direction
layers (X&Y)  equivalent of 5x5 mm2 (SSA)
Read out by SiPM
A physics prototype with a deported electronics was built and successfully tested
A technological prototype is being developed with
Scintillator shape that optimizes light collection and reduces dead zones : rectangular, wedge, tapered..
SiPM more compact with higher linearity range
and less noise (MPPC 10000 ch in 1x1mm2)
Electronic board to host ASIC on one side
and scintillator plane on the other.
A first plane with the new technology was tested
in 2014.
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
Linearity <1.5%
Energy resolution
12.8%/E ⊕ 1.0%

## Slide 29
Technologies proposed for ILD&SiD calorimeters
HCAL for ILD
48 layers of 2 cm stainless steel interleaved with
planes made of 3x3 cm2 tiles, read out directly by SiPM
and embedded electronics.
A physical prototype of 38 layers of 1 m2, totalizing
(5.3 lI) accompanied by a tail catcher (6 lI) with
deported electronics was built and successfully tested
A technological prototype fulfilling the ILD requirements is being developed :
Optimized tile shape for direct readout
Embedded, power-pulsed readout electronics
Large plane with tiles assembled in a way to reduce
dead zones
Self-supporting mechanical structure
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
Several planes of different sizes were made and successfully tested in 2014

## Slide 30
Technologies proposed for ILD&SiD calorimeters
HCAL for ILD
48 layers of 2 cm stainless steel interleaved with
planes made of Glass RPC and their embedded readout 2-bit electronics allowing a lateral segmentation of 1 cm2
A technological prototype of 48 fulfilling almost all the ILD requirements of compactness and power consumption was built with a self-supporting mechanical structure. It ws successfully tested with
Triggerless mode
Power-pulsing mode
Last step is to build very large GRPC and equip them with the last generation of the readout electronics
The GRPC was also successfully tested in a magnetic field of 3 T using the power-pulsing mode
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation

## Slide 31
Technologies proposed for ILD&SiD forward calorimeters
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
LumiCal: Precise luminosity measurement (10-3) at 500 GeV.
BeamCal : Instantaneous luminosity measurement, beam diagnostics
but very high radiation load (up to 1MGy/ year)
LHCaL: Extends the calorimeter measurements to small polar angles
LumiCal (31 -77 mrad)
Two Si-W sandwich EM calo at ~ 2.5 m from the IP (both sides).
30 tungsten disks of 3.5 mm thickness. Si sensor pitch of 1.8 mm
Two tracking layers in front are envisaged to improve angle
measurement and separate e/g.
BeamCal (5 – 40 mrad)
similar W-absorber as for the LumiCal but radiation hard sensors
(GaAs, CV Diamond, Sapphire, Si).
Segmentation is being worked out,
new ideas on the sensor orientation

## Slide 32
Technologies proposed for ILD&SiD forward calorimeters
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
LumiCal chip in 130 nm.
● 8 channel (preamp, shaper Tpeak ~ 60 ns,~9 mW channel);
● 8 channel pipeline ADC, ~1.2 mW/MHz;
● FPGA based data concentrator and further readout.
4 layers are realized and tested in TB
Mechanical structure studied and prototyped
BeamCal
Choice of the sensor will depend on the T-506 studies at SLAC
BeamCal is sensitive above 50 GeV. At 50 GeV the fake rate due to beamshtrahlung is 0.5% for R>7 cm,
energy resolution = 10%, at 200, 4% at 500
GeV 4%

## Slide 33
Technologies proposed for ILD&SiD muon detectors
For ILD
14 (12) active layer for the barrel (endcap ) region, interleaved with iron slabs of return yoke.
Baseline adopts scintillator strips read out by SiPM through WLS fibers. RPC are an alternative (X&Y)
For SiD
Similar scenarios
More work is needed in this field

## Slide 34
Cost estimate

## Slide 35
Cost estimate

## Slide 36
Conclusion
A tremendous amount of work on the ILC detectors has been achieved.
Many technologies have reached maturity.
Work on engineering prototypes is ongoing.
Common developments on the DAQ have been initiated.
Installation scenarios of the different sub-detectors are under study.
Many R&D within the ILC framework have been adopted in other experiments (upgrade LHC, BELLEII, STAR…)
R&D for ILC could benefit other future lepton colliders
CLIC, CPEC,FCC ee even if some features associated to
different duty cycles need to be carefully studied.

## Slide 37
Acknowledgement
This presentation is a summary of many presentations by the different members of the ILD and SiD collaboration.
I apologize if information of some R&D are not be up-to-date

## Slide 38
Back up

## Slide 39
ILD PFA performance

## Slide 40
Resolution
Tracking
Leakage
Confusion

## Slide 43
ILD

## Slide 44
ILD cost

## Slide 45
Metal 1 Shield Traces
Terraced View
Au pads